## Slide 1
Building the Boom Arm Extracellular Electrode Holder
Designed by Dr. James Ryan for the CrawFly Collective

## Slide 2
Step 1: 3D print the parts for the boom arm
Parts A, B, C must be printed with supports
Parts should be printed with at least 50% infill for strength and rigidity
The two screws (F) should be printed at 100% infill.
.stl files for the parts are available on our GitHib at:
https://github.com/CrawFly/DIY-Neuroscience
A
B
C
D
E
F
F
G

## Slide 3
Step 2: Prepare the base.
There are two options for bases:
1) A 4x4 inch sheet of 1/8th or ¼ inch steel plate. Available at Lowes or Home Depot
2) An On-Off magnetic base (used if you have a steel table).
1
2
Can be purchased from Harbor Freight for ~$13.00 US

## Slide 4
Step 3: Superglue 3d printed part E to the center of either the steel plate or the top of the magnetic base.
Step 4: Prepare the two x-y microscope stages
Begin by removing the slide holders from the top and the scales from the top and bottom sections as shown on the right

## Slide 5
Step 5: Remove the x axis from the y axis by removing the two sliver screws
At this point you should have 2 x-axis parts that look like the one on the right in this photo.
You should also have 2 of the y-axis components (used later).

## Slide 6
Step 6: Using a hacksaw or band saw, cut the left side of the x-axis off as shown in the photo.
Repeat this process for both x-axis components

## Slide 7
Step 7: Use superglue or epoxy to glue 3D printed part E to the center of the base (either the metal plate or the magnetic base).
Step 8: Use superglue or epoxy to glue part G to the top of one of the x-axis components. It should be in line with the x-axis component. Be sure not to get glue into the moveable parts of the x-axis.
E
G
X-axis 1
X-axis 2
Step 9: Glue x-axis 2 to part G so that the thumb screws are 90 degrees to x-axis 1 (see photo).

## Slide 8
Step 10: Glue 3D printed part A on top of x-axis 2. The center post with the hole should be in line with the x-axis component
Part A

## Slide 9
Step 11: Prepare 3D printed parts C, D, and F as shown below on the left. Place parts C and D over the upright section of part A and thread the screw through the holes. Make sure part D locks into the boom arm and that the rough side of part D is against the rough side of part A.

## Slide 10
Step 12: Slide 3D printed part B over the end of the boom arm (part C) and thread the second screw (F) through the holes.
Step 13: Glue one of the y-axis components into the slot in part B. Be careful not to get glue into the mechanism